## Slide 1: Before we begin…
Q: Who are the stakeholders that are interested?
A: Imagine all of you are part of BCA, HDB.

## Slide 2: Evaluating Effectiveness of Cool Coating on Outdoors Environment
LIM ZHENG WEI
LEAD DATA SCIENTIST FOR “COOL SINGAPORE”

## Slide 3: Background
Vegetation removed
High-rise buildings block air circulation, absorb heat
Urban Heat Island (UHI) Effect
Inefficiencies in Generators
More population living in urban regions
3% in 1800 vs 61% projected by 2030 (Hien & Ignatius, 2016)
Responsible for up to 70% of greenhouse emissions (Hoornweg, Freire, Lee, Bhada-Tata, & Yuen, 2011)
Notes: In 1800, 3% of world population stayed in urban regions
By 2030, projected 61%/5b people
Transition from rural to urban areas has huge environmental repercussions
Urban areas are responsible for up to 70% of greenhouse emissions
Vegetation removed to make way for high-rise buildings
They block the wind and have massive surfaces to soak up the solar heat in the day and release them in the night
When it’s hot, we turn on a/c
Very hot days can create enormous energy spikes, further bolstering the hear
Because inefficiencies in electricity generation, waste energy converted to heat energy

## Slide 4: Impacts of UHI
The temperature is higher in over-developed areas
Increased demand for air conditioning
Further heating, CO2 release
Thermal Comfort, Health & Environmental Quality drops
UHI Effect worsens
Notes: This issue will be further provoked by the increasing demand for air conditioning,
which will repeatedly lead to further heating and carbon dioxide release.
UHI affects street level thermal contentment, health and environmental quality and may increase energy demand. With more infrastructure and a
continuous rise in population, the temperature will continue to rise. Therefore, there is a need to
minimise the heat being soaked up by the surfaces’ of the building.

## Slide 5: Existing Solutions
Trees and vegetation (Ballinas & Barradas, 2016)
“Cool” roofs and pavement (Alchapar, Correa, & Cantón, 2014)
Urban planning with UHI consideration (Maimaitiyiming, et al., 2014)
Notes: Currently we have 3
1) Trees and vegetation
A vast study on greenery has shown that trees and vegetation cover lower surface and air temperatures by providing shade and a cool environment through evapotranspiration. Furthermore, the recent trend of growing a vegetative layer (plants, shrubs, grasses, and/or trees on the roof (green roofs) and building façade (vertical greenery) reduces the temperatures of the building envelope and the surrounding air.
2) ‘Cool’ roofs and pavement
By installing a ‘cool’ roof using materials or coatings that significantly reflect sunlight and heat away from a building can help to reduce roof temperatures, increase the comfort of occupants, and lower energy demand. Moreover, using ‘cool’ paving materials (for sidewalks, parking lots, and streets) not only cools the pavement surface but also the surrounding air, reducing overall outdoor temperature.
3) Proper city planning that implements UHI mitigation strategies is required, either by strategically designing open spaces with greenery or regulating the construction of building materials that meets the standard derived from the UHI studies.

## Slide 6: Research Gap, Objective , Scope
Research Gap
Experiments conducted in small scale
Different climate
Objective
Assess effectiveness of cool coating on urban thermal balance
Scope
Analyse surface temperatures on roofs, pavement and walls
Notes: This study assess the effectiveness of nature of reducing UHI effect by using different
types of plants incorporated onto the rooftops of buildings in the CBD areas under varying
structure conditions. The effect was investigated by analysing the surface temperatures on the
roof of the buildings. Data collected was be compared to the temperatures of buildings without
greenery systems within the area of the test site.

## Slide 7: Proposal of Methodology
A) Collection of Data
  1) Hydrotransmitter - humidity and temperature
  2) Air velocity transmitter - air velocity
  3) Datalogger – records
  4) Pyranometer - solar irradiance
  5) Pyrgeometer – radiation
  B) Duration: 3 months
  Time interval: 5 minutes
Notes: A couple of apparatus was used to help to record the essential criterions; Hydrotransmitter to measure humidity and temperature, air velocity transmitter to measure air velocity, datalogger to take down the records, pyranometer to measure solar irradiance, and pyrgeometer to measure radiation ranging from 4.5 to 100 micrometres.

## Slide 8
Block A
Block B
Block C
Block D
Control
With coating

## Slide 9: Potential Challenges
1) Site to conduct experiment
2) Installation of equipments

## Slide 10: Conclusion
1) Expected to succeed
2) Cut in energy consumption, saving cost
Future work: Use data to show correlation between cool coating and cost of energy consumption
Notes: Based on past experiments and experiences, it is expected that this implementation will be a success

## Slide 11: Reference
Hoornweg, D. A., Freire, M., Lee, M. J., Bhada-Tata, P., & Yuen, B. (2011). Cities and climate change: Responding to an urgent agenda. Washington, D.C.: World Bank. doi:10.1596/978-0-8213-8493-0
Hien, W. N. (n.d.). A Study of Urban Heat Island in Singapore. Retrieved from http://www.sde.nus.edu.sg/rsh/SDE_rsh_highlights_B01.html
Ballinas, M., & Barradas, V. L. (2016). The Urban Tree as a Tool to Mitigate the Urban Heat Island in Mexico City: A Simple Phenomenological Model. Journal of Environment Quality,45(1), 157. doi:10.2134/jeq2015.01.0056
Alchapar, N. L., Correa, E. N., & Cantón, M. A. (2014). Classification of building materials used in the urban envelopes according to their capacity for mitigation of the urban heat island in semiarid zones. Energy and Buildings,69, 22-32. doi:10.1016/j.enbuild.2013.10.012
Maimaitiyiming, M., Ghulam, A., Tiyip, T., Pla, F., Latorre-Carmona, P., Halik, Ü, . . . Caetano, M. (2014). Effects of green space spatial pattern on land surface temperature: Implications for sustainable urban planning and climate change adaptation. ISPRS Journal of Photogrammetry and Remote Sensing,89, 59-66. doi:10.1016/j.isprsjprs.2013.12.010